## Slide 1: Problem: Autonomous Perception for Terrain Classification
Forward-looking Terrain Classification
  Goal: Identification & Segmentation of Terrain Features and Areas
  Reach goal: Real-time Estimation of Terrain Trafficability
  Cost-map Generation for Autonomous Navigation

## Slide 2: Problem: Autonomous Perception for Object Classification
Forward-looking Object Classification
  Goal: Identification & Segmentation of Objects
  Reach goal: Real-time Estimation of Obstacle Trafficability
    E.g. Vehicle-dependent cost for driving over bush vs. tree
  Cost-map & Occupancy Grid Generation for Autonomous Navigation

## Slide 3: Exteroceptive Sensors
Public Dataset Sensors
Camera: Basler Ace
  Model: acA1920-50gc
  1920x1200, 50fps
  16mm Prime Lens
Lidar: Ouster OS1
  Model: OS1-64
  64 Chan, 45⁰ Vertical FoV
  2048 Horizontal Res., 10Hz
AVT-341 Sensors
Camera: Flir Oryx
  Model: ORX-10G-51S5C-C
  2448x2048, 162fps
  Lens TBD
Lidar: Velodyne VLP
  Model: VLP-16
  16 Chan, 30⁰ Vertical FoV
  900-3600 Horizontal Res., 5-20Hz

## Slide 4: Publicly Available Datasets for Unstructured Environments
RUGD
Variety of Terrain Types
Only Camera Image Annotations
Rellis-3D
Similar Terrain Type
Camera Image and Lidar Annotations
Synchronized data from:
    Stereo Camera
    Velodyne and Ouster Lidar
    Mono Camera

## Slide 5: Machine Learning Architectures
Echo State Network (ESN)
Reservoir Computing Architecture
Transforms linear data into high-dimensional state space
Very short training times! (only output layer is trained)
Recurrent Neural Network (RNN)
Long training times
Requires high computing power

## Slide 6: Modified Echo State Network
The use of multiple smaller parallel and/or series reservoirs that split the input image into equal portions.
The total neuron count is the number of parallel reservoirs multiplied by the neurons per reservoir.
The neuron states of each parallel reservoir is concatenated into a single state vector.
Split the image into equal parts…
Augment the data…
Run through the reservoirs…
Faster ESN performance!

## Slide 7: Modified ESN for Image Data
ESN programmed in MATLAB
Robot Unstructured Ground Driving (RUGD) Dataset[11]
ESN Parameters | Value
Train/Test Samples | 60
Neurons | 100
Parallel Reservoirs | 16
Input Scaling | 0.0002
Spectral Radius | 0.0001
Learning Rate | 0.04
Time Steps | 60
Res. Connectivity | 10%
[11]Wigness, M., Eum, S., Rogers, J. G., Han, D., & Kwon, H. (2019). A RUGD Dataset for Autonomous Navigation and Visual Perception in Unstructured Outdoor Environments.

## Slide 8: Optimization w/ Modified ESN for image data
Hyperparameter optimization with grid search takes only 30 minutes!
Error minimum = 6%; Train Time = 200 s (3 min 20 s)
  69 parallel reservoirs
  760 neurons per reservoir

## Slide 9: Modified ESN for Lidar Data
ROS2 input and output
PointCloud input features
  [x y z intensity]
  Other features exist
PointCloud sizes
  4.2 MB / PCL
  4 times camera image size
Gaussian Noise
  SNR = 10 (not optimized)

## Slide 10: Modified ESN for Lidar data
RELLIS-3D Dataset*
*Jiang and al., “RELLIS-3D Dataset: Data, Benchmarks and Analysis”, arXiv, 2020
Programmed in MATLAB
24 classes relabeled to 4
Trafficability | RGB Color | Cost Value
High | [0, 255, 0] | 0
Medium | [255, 255, 0] | 0.33
Low | [255, 128, 0] | 0.67
Zero | [255, 0, 0] | 1

## Slide 11: Modified ESN for Lidar data
Criteria | Performance
Avg. Class. Rate | 83.1%
Training Time | 31 min.
Avg. Class. Time | 1.9 sec.
L-ESN Parameters | Value
Train/Test Samples | 120
Neurons | 400
Parallel Reservoirs | 16
Reservoir Connectivity | 10%
Spectral Radius | 0.008
Learning Rate | 0.08
Time Steps | 30

## Slide 12: Motivation: Camera – Lidar Fusion
Lidar provides 3D Point Cloud
  Difficult to train for reliable classification
  Active sensor modality (“beacon” for adversaries)
Mono Camera provides pixel-wise Semantic Segmentation w/ Classifications
  2D image…needs additional information to be mapped to 3D space
  Passive sensor modality (sensitive to lighting conditions)

## Slide 13: Camera + Lidar Perception Node
Raw Lidar PCL
Image to Point Cloud
Raw Camera Image
Image Segmentation
Deeplab V3+
Fuse
2D Cost Map
Global Accuracy | Mean Accuracy | Mean IoU | Weighted IoU
0.9113 | 0.9401 | 0.5906 | 0.8602
Deeplab V3+ Train/Test Global Results
Vehicle

## Slide 14: Mapping/Planning Integration
Arbitrary Cost Assignment based on Classification
Output data types:
  Matrix array
  VehicleCostMap object
VehicleCostMap object​
Matrix array